## Slide 1: CellProfiler: An introduction to object detection, measurement and batch processing
Dr. Dominic Alibhai & Dr. Stephen Cross
Download “Example data” from https://goo.gl/rQpywN

## Slide 2: Overview
Introduction to CellProfiler
  What is it?
  Looking at modularity and batch processing
  Image and object models
  Tour round the interface and key features
Live demo of example workflow
  Detecting cells and bacteria
  Counting the number of bacteria per cell
  Drawing detected objects on the input image
  Outputting results as images and spreadsheets

## Slide 3: Where to get help
CellProfiler software
  Detailed integrated documentation
Websites
  http://cellprofiler.org/manuals/
  http://cellprofiler.org/tutorials/
Wolfson Bioimaging!
  Stephen: stephen.cross@bristol.ac.uk
  Dom: da14205@bristol.ac.uk
  Office: C31 (Biomedical Sciences Building)

## Slide 4: What is CellProfiler?
Modular
Scalable
Flexible
Reproducible
Image data
Object data
Share pipelines
Batch processing
Reads metadata
Grouping by condition, plate or experiment
CellProfiler
Drag and drop modules
Easily editable for new experiment
Extendable
Open source
Python
Intensity values
Shape parameters
Save pipelines

## Slide 5: Modularity and batch processing
Load in images
Save images
OUT
Filter images
IN
OUT
IN
Find nuclei
OUT
IN
Loop over all images

## Slide 6: Image and object data
Image data
Object data
Pixel array, e.g 512 x 512
Intensity value per pixel
Pixels independent
Pixel array, e.g 512 x 512
Intensity value per object
Shape parameters per object
Pixels are grouped into objects

## Slide 7: Quick note on CellProfiler3
CellProfiler is currently undergoing a major upgrade to version 3
  Adds 3D native support
  Currently not all modules work in 3D
  Standard 2D modules should be fine

## Slide 8: CellProfiler interface
List of modules
Module notes
Compulsory modules
Optional modules
Module parameters
Parameter help
Current module help
Enter “test mode”
Run full analysis
Enable/disable visualisation
Module status

## Slide 9
Live demo
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 10: Image loading
Adding files
  Right click “Drop files and folders here”, then “Browse for images”
File filters
  Images only
  Specific file extensions
  Names including specific text
  Names matching patterns

## Slide 11: Metadata
What is metadata?
  Information describing the image
  Examples: number of channels, well name, spatial calibration
Where’s this info stored?
  Separate file
  File header
    Encoded at the start of the file
  File name
    Name written using specific pattern

## Slide 12: Names and types
Group files by metadata value
  Assign each group a name
  Groups can be processed differently
For example, our three channel test image
  Group 1: nuclear stain (“Blue”)
  Group 2: actin stain (“Green”)
  Group 3: bacteria (“Red”)

## Slide 13: Grouping
Higher order grouping than with “names and types”
  Useful for grouping by well, plate, condition, etc.
Groups will be processed separately
Can group by multiple fields

## Slide 14: Adding modules
To add modules
  Right click module area
  Select module of choice
To remove modules
  Highlight module
  Press “Delete” on keyboard
To move modules
  Drag module to new position in list

## Slide 15: Test mode
Test mode allows each module to be evaluated on its own
Useful for testing parameters
To use test mode
  Click “Test mode”
  Sequentially evaluate each module by clicking “Step”
  When a module is changed, the current position will return here

## Slide 16
Worksheet section 1
File loading
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 17: Identify primary objects
Objects that are typically isolated
  Found by applying an intensity threshold and identifying contiguous regions
  Don’t require a marker to assist localisation
Can refine identification
  Size filters
  Watershed segmentation (object splitting)
Examples of primary objects:
  Nuclei, bacteria, cilia
Notes: Live: Show detection using basic settings – which looks poor, then switch to advanced settings

## Slide 18: Identify primary objects
Typical diameter of objects (size filter)
Threshold strategy (global or “adaptive”)
Thresholding method (Otsu, etc.)
  Method-specific parameters will be shown
Method to distinguish clumps
  Shape will split at necks in objects
  Intensity is good for blobs/spots
  Can specific minimum separation for splitting
Notes: Live: Show detection using basic settings – which looks poor, then switch to advanced settings

## Slide 19
Worksheet section 2
Identify primary objects
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 20: Identify secondary objects
Uses previously-identified objects as markers for detection
Many methods for detecting object edges
  “Propagate” moves object boundary out from marker at constant rate
  “Watershed” uses image intensity
  “Distance” creates fixed range around marker
Used for detecting cells from marker nuclei
Notes: Live: Show detection using basic settings – which looks poor, then switch to advanced settings

## Slide 21: Identify tertiary objects
Creates objects from the difference between two other objects
Used for identifying cytoplasm from previously-identified cells and nuclei
Notes: Live: Show detection using basic settings – which looks poor, then switch to advanced settings

## Slide 22
Worksheet section 3
Identify secondary and tertiary objects
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 23: Smooth (filter) images
Apply filter to image to reduce noise
Various filters including
  Polynomial, Gaussian, median, average
Automatic or manual radius calculation
  Automatic is 1/40 the image size (and no more than 30 pixels)

## Slide 24: Measure image/object properties
Measure properties such as
  Object size/shape
  Intensity/texture (intensity values are normalised)
  Colocalisation
Measurements are assigned to the image or object
Measurements can be used in subsequent modules

## Slide 25: Filter objects
Remove objects based on previous measurement
Specify threshold value
Create new object for the retained objects

## Slide 26: Relate objects
Assign relationships between objects based on spatial overlap
One “parent” object can have multiple “child” objects
Can calculate mean values for child object measurements

## Slide 27
Worksheet section 4
Apply measurement-based object filters and relate objects
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 28: Overlay outlines / display data
Overlay outlines
  Create image showing object outlines
  Can display on either a blank image or other previously-loaded image
  Add outlines for multiple object sets
Display data on image
  Add measurement values to images
  Text centred on object

## Slide 29
Worksheet section 5
Visualising data
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 30: Save images
Names based on input image
  Takes name from input image
  Add custom suffix
Specify output location
  Specific folder
  Same folder as input
  Default location (set via File > Preferences…)

## Slide 31: Convert objects to image
Creates a image showing objects
Option for indexed images
  Intensity of each pixel corresponds to ID number of object
Color format
  “Color” uses random colouring
  “Binary” are black and white
  “Greyscale” are indexed (up to 255 objects)
  “uint16” are indexed (up to 65535 objects)

## Slide 32: Export to spreadsheet
Multiple exported files
  One per object set
  Object relationships summary
  Analysis pipeline summary
  Can choose which to export
Specify output location
Add prefix to filename
Select measurements to export

## Slide 33
Worksheet section 6
Exporting data
Notes: 45 minutes
Wait 10 minutes
16:40

## Slide 34: Regular expressions (Regex)
Filenames have specific pattern
  e.g. “Image_B3_F1.tif” is “[Name]_[Well]_[Field].tif”
Regex extracts this information
  Assign regions of name to different metadata values
CP has a handy regex editor
  Click the magnifying glass
  Colours identified part of name

## Slide 35: Other courses
ImageJ/Fiji Level 1
  Basics of image processing and analysis
  15th May 2019
ImageJ/Fiji Level 2
  Automation and batch processing using macros
  29th May 2018
Book via OnCourse (www.cbs-bris.org.uk)